## Slide 1: 5-minute CHERI Primer
Far too many people to name on one slide in readable text

## Slide 2: CHERI capabilities grant access to memory
s
pointer (64 bits)
256-bit capability
Virtual
address space
v
1-bit tag
permissions (31 bits)
objtype (24bits)
length (64 bits)
offset (64 bits)
base (64 bits)
Tag in registers allows type-oblivious copying (e.g. memcpy)
More than required
Lots of redundancy
Notes: Note: 256-bit version shown for clarity, most work is using the 128-bit compressed representation.

## Slide 3: All memory accesses require a capability
MMU
Physical Memory
Physical address
$Cn
Checked
virtual address
Capability
Load / Store
Instruction
Fetch
Legacy
Load / Store
Virtual address
$PC
$Rn
$PCC
$DDC

## Slide 4: Sealing gives opaque pointers
Sealing Capability
Data
Capability
Sealed Capability
Seal
Unseal
Data
Capability
Trusted code
Trusted code
Untrusted code
Unseal
Other data
Trap!
Notes: Trap will become null soon. Talk more about co-design!

## Slide 5: Binary compatibility
Legacy code lives side-by-side with CHERI code
Incremental adoption options – e.g., shifting to capabilities for return addresses, just stack pointers, etc.
More compatible
Safer
Legacy
All pointers are integers
Hybrid
Some pointers are capabilities
Pure-capability
All pointers are capabilities

## Slide 6: Teaching a production compiler that pointers are not integers
David Chisnall

## Slide 7: The high-level problems?
Does your source language understand the difference?
Does your IR understand?
  Do optimisers respect this?
Does your back end preserve the distinction?

## Slide 8: CHERI C
CHERI provides:
  128-bit capabilities
  Unforgeable
  Bounded
  Contain permissions
We want to use these as the target’s representation of C pointers

## Slide 9: What do these mean?
void *x = …;
intptr_t iptr = (intptr_t)x;
long l = (long)x;
void *y = (void*)(iptr + 42);
if (iptr % 4 != 0) { … }
y = (void*)l;
y = (void*)(iptr + iptr);

## Slide 10: LLVM IR looks very clean
Fixed-size integer types (e.g. i8, i32, i128)
Pointer types (e.g. i8*, i8**)
But two instructions are problematic:
  inttoptr
  ptrtoint
Underspecified semantics, effectively a bitcast
Notes: Non-integral pointer mode disallows inttoptr / ptrtoint entirely

## Slide 11: Optimisations make assumptions
Partial writes to pointers are allowed
Loads can be widened if they don’t span cache lines
An n-bit pointer can address 2n bytes of memory
Pointers have known bit representations
Casts are commutative
Lots of small fixes needed!

## Slide 12: Back ends make it worse
LLVM type legalisation lowers pointers to integers
Needed to introduce new pointer types…
…but then most things just worked.

## Slide 13: The result: CHERI LLVM
Around 8KLoC changes in clang
  Excluding tests, including new warnings
Around 8.5KLoC changes in LLVM
  Excluding tests
  Including around 6KLoC in the MIPS back end
Lots more in runtime libraries (libUnwind, libcxxrt, libobjc, libc, and so on).
Provides spatial memory safety for [Objective-]C/C++